## Slide 1
OFF-ROAD EV PLATFORM
Powertrain modelling, control and validation on a real vehicle
KICKOFF REVIEW POL CRUAÑAS · SEPTEMBER 2026

## Slide 2
What this project is
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
02
An electric mini-quad, used as a bench for power electronics, machines and control. The hardware is finished — the work is modelling it and controlling it.
THE PLANT
The vehicle. It exists and it runs.
THE DIGITAL TWIN
A Simulink model, parameterised from measurements.
THE ENGINE
A two-week cycle, closed by a review with you.
WHAT ALREADY TRANSFERS
— Test benches and measurement campaigns
— Torque and efficiency maps
— Correlating a model against real hardware
WHAT DOES NOT
— Power electronics
— Electric machines in the rotating dq frame
— Embedded control and software architecture

## Slide 3
The vehicle
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
03
Nitro Motors mini-quad: 36 V lead-acid → 48 V lithium.
Mass, with driver
≈ 112 kg
Wheels
13 × 5.00-6 · r ≈ 0.155 m loaded
Final drive
chain 25H · 11T / 92T = 8.36:1
Battery
13S5P Li-ion · 48.1 V · ~13 Ah
Motor
48 V PMSM · ~1.9 kW · 3 pp
Peak wheel torque
76 N·m at 120 A
WHY 92 TEETH

## Slide 4
System architecture — as it is today
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
04
The twist grip drives the inverter directly. Nothing sits between the driver and the torque, and nothing records what happens under load.

## Slide 5
System architecture — where it is going
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
05
A vehicle control unit takes the driver inputs — brakes included — and sends a torque request over CAN.

## Slide 6
The powertrain, component by component
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
06
BATTERY
— 13S5P Li-ion · 65 cells
— 48.1 V · ~13 Ah
— JK smart BMS · 40 A
WHY THIS ONE
Configurable and observable: every cell voltage readable from the phone while the vehicle runs.
INVERTER
— Flipsky FSESC 6.7 Mini Pro
— 70 A cont. · 200 A peak
— FOC · 30 kHz · CAN
WHY THIS ONE
Open source. I can read the firmware line that computes the torque, and export the whole configuration to XML — which is what parameterises the model.
MOTOR
— 48 V PMSM · ~1.9 kW
— 3 pole pairs · Hall
— Urban Fox scooter donor
WHY THIS ONE
Came with the donor, and is not confirmed on paper. It is the component the whole model hangs on, so it had to be measured.

## Slide 7
Where the limits actually are
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
07
BATTERY
40 A → 1.9 kW
this is the ceiling
MOTOR
120 A → 9.1 N·m
no thermal protection
VOLTAGE
0.95 × 48 V
sets top speed
WHAT THAT MEANS FOR THE MODEL
The inverter, 70 A continuous, never shapes this curve — it limits how long the flat part can be held. The battery gets only what it takes to set the ceiling: no thermal model, not this year.

## Slide 8
What the model needs, and where it comes from
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
08
Three equations. Every symbol in them is a number someone has to go and measure.
MEASURED ON THIS VEHICLE
p
3
Hall pulse count
λm
16.86 mWb
back-EMF, scope
Kt
0.0758 N·m/A
derived from p and λm
R
28.0 mΩ
inverter detection
Ld / Lq
99 / 113 µH
inverter detection
J
1.56·10⁻⁴ kg·m²
spin-down
T₀ / b
63 mN·m / 139 µN·m·s/rad
spin-down
None of this came from a datasheet. The datasheet was wrong.

## Slide 9
How the machine was measured
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
09
POLE PAIRS
Counted the Hall pulses over one turn of the sprocket: 25 against 25.1 predicted for p = 3, and 33.5 for p = 4.
FLUX LINKAGE
Motor off the inverter, dragged by a drill, scope across two phases. Two speeds agree to 0.17 %.
INERTIA AND DRAG
Three spin-downs anchored on the steady no-load point: J = 1.56·10⁻⁴ kg·m², plus dry and viscous friction.
Next: a coast-down on the vehicle — rolling resistance, drag and vehicle inertia in one test. That is what the straight-line model needs.

## Slide 10
How I learn, and what I refuse to delegate
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
10
DERIVE IT
A dragged-in FOC block gives a quad that works and an engineer who learned nothing.
Clarke and Park
the current loop
vehicle dynamics
COPY IT
No first principles there, and no shame about it. The budget for deriving goes where the learning is.
build systems
protocols
drivers
file formats
LET THE AI FILE IT
Never the reasoning. An agent that hands me a conclusion I should have reached has negative value.
notes and plots
traceability
formatting
my own slips
One Git repository holds the measurements, the decisions and the reasons behind them. Nothing important lives only in my head.

## Slide 11
How the work is organised
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
11
THE 45 MINUTES WITH YOU
5 min
What I said I would do
15 min
What I did, with data
10 min
What I do not understand
10 min
Does the reasoning hold?
5 min
Goal of the next cycle
The middle twenty minutes are the point. A review where I only show what worked wastes two doctorates.
If I cannot explain it out loud without notes, the cycle is not finished.

## Slide 12
The plan to December
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
12
AFTER C06 · 2027
Control on the ESP32 · Traction and launch control · MPC on a validated model
End of 2026: a model validated against the real vehicle.
The machine came in ahead of plan, so C01 moves on to the vehicle.

## Slide 13
What I need from you
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
13
Three things. They are worth more to me than technical answers.
01
Hold me to a date
Without an external deadline I postpone indefinitely. The date being fixed is the mechanism — the meeting itself is secondary.
02
Attack the reasoning, not the result
Do not ask whether the number is right. Ask why I chose that method, and what would have to be true for it to be wrong.
03
Tell me when I explain badly
If an explanation does not land, that is usually not a language problem. It is me not having understood it.
What I am not asking for: that you validate field-oriented control or electric-machine theory. That gap I close elsewhere — you are not being examined on a domain that is not yours.

## Slide 14
What I am asking for today
OFF-ROAD EV PLATFORM · Kickoff review · September 2026
14
12 Oct
First full review
C01 — closing the vehicle side
Every 2 weeks
Cadence
Monday, 45 minutes, six reviews to December
3 of 3
Machine parameters measured
pole pairs · flux linkage · inertia
Confirm the slot, and I will put all six review dates in the calendar before I leave.